# About

This document describes the adapter and its processes.

# Adapter Configuration

In your application settings.py add the following dictionary script
HIFADHI = {
    "gossip_instance": "127.0.0.1",
    "port" : 80,
    "password" : "demopassword",
    "algorithm" : "balanced"
}

The first three keys are self explanatory, as for the algorithm there are 2 possible options, Round Robin and Balanced. The algorithm defines how to determine the instance to store given data to.
# Adapter Workings
The adapter communicates with the gossip instance through TCP.
Upon initialization it tries to retrieve the list of available instances, to which it will get a 401 or 200 response. The list of available instances is received as JSON of instances of the following format.
{
    "instance_name" : {
        "location" : "Ipv4",
        "total_secondary_memory" : 1289323,
        "available_secondary_memory" : 89434,
        "total_main_memory" : 837843,
        "available_main_memory" : 23213
    }
}

The endpoint to obtaining this list is documented in the instance documentation. If a 401 response code is received the adapter will throw an exception.
From there it provides methods that will be used to upload a file, delete a file and handle access control.

# Adapter Methods

getInstances() → retrieves instances from the gossip server
uploadFile(file,filename,access) → uploads a file to any of the available instances
Optional parameters :
mode → allows us to define the if the file should be automatically cached on all	instances for high availability. Available modes are
  high_availability: Caches on all instances
  high_availability_in_memory Caches on all instances in main memory.
Responses:
200 → Returns a query string.
*
signFile(query_string,duration) → generates a pre-signed query string that is valid for the	duration
Response:
200 → Returns a pre-signed query string
*
ipv4Access(ipv4,duration) → gives access to a file to the provided Ipv4 for the provided duration.
Responses
200 → Returns the access identifier string.
Notes:
If the instance is behind a load balance the received Ipv4 will be that of the ALB, there	one should add the header FOWARDED_FOR which contains the Ipv4 for the client.
deleteSignature(signed_query_string) → Deletes a given signature
Responses:
*
deleteIpv4Access(access_identifier_string)
Responses:
*

deleteFile(query_string)
Responses:
*

setHighlyAvailable(query_string,boolean) → Caches a file on all servers if true and vice versa for	false
Responses:
200 → A string list of the instances the file was cached
*
Notes:
The file is removed based on the algorithms defined in the instance documentation. The
delete method removes the file from all caches.

setHighAvailabilityInMemory(query_string,boolean) → If true moves a file into main memory of all	instances.
Responses:
200 → Instances where the file is now in main memory.
*